## Slide 1: MINES-VIS
Week 1

## Slide 2: Minor Embedded Systems
Modules
  MINES-ROB: Robotics
    Advanced Control: learn to realize intelligent behavior
  MINES-VIS: Vision
    Advanced Sensing: learn to extract information from camera images. You will not learn how to program in C++ or other languages
  MINES-CON: Connectivity
    Advanced Connectivity: learn to apply adhoc wireless networking
  MINES-INNO: Innovations in Embedded Systems
    Research: learn to investigate new ES technology
Projects
  MINES-PROJ: Project ES

## Slide 3
Connections to other disciplines

## Slide 4
Where am I
where are you
How do I get there?
A goal oriented machine that can sense, plan and act.
Robot a definition:
Project ES example

## Slide 5
Topics
Image sensing & Acquisition
Representing digital image(greyscale)
Image processing,
Histograms,
Thresholds,
Smoothing, blurring,
Blobs, area and centroid
TOPICS in brief week 1

## Slide 6
Learning OpenCV Computer Vision with the OpenCV Library. Gary Bradski & Adrian Kaehler ISBN: 978-0-596-51613-0
Computer Vision Algorithms and Applications. Richard Szeliski. ISBN: 978-1-84882-935-0
Digital Image Processing. Rafael C. Gonzalez & Richard E. Woods ISBN:978-0-13-168728-8
Machine Vision: Automated Visual Inspection and Robot Vision” http://homepages.inf.ed.ac.uk/rbf/BOOKS/VERNON/
Recommended reading:

## Slide 7
A digital image is a representation of a two-dimensional image as a finite set of digital values, called picture elements or pixels.
Image Acquisition and Formation Model
Notes: Illumination and Reflection

## Slide 8
Image Sensing and Acquisition

## Slide 9
The relative quantity of photons in each cavity are sorted into various intensity levels, whose precision is determined by bit depth (0 - 255 for an 8-bit image).
Each cavity is unable to distinguish how much of each color has fallen in, so the above illustration would only be able to create grayscale images.
A Bayer(color filter) array consists of alternating rows of red-green and green-blue filters
Image Sensing and Acquisition
( Filter)

## Slide 10
Bit depth quantifies how many unique colors are available in an image's color palette in terms of the number of 0's and 1's, or "bits," which are used to specify each color
BIT DEPTH
Every color pixel in a digital image is created through some combination of the three primary colors: red, green, and blue.
8 bits
24 bits
Image Sensing and Acquisition

## Slide 11
BIT DEPTH
Image Sensing and Acquisition

## Slide 12
Pixel values typically represent gray levels, colours, heights, opacities etc.
Remember digitization implies that a digital image is an approximation of a real scene
1 pixel
An image may defined as a two-dimensional functions of the form .
x and y are spatial (plane) coordinates, and the value or amplitude of f at any pair of coordinates is a positive scalar quantity.
Image Acquisition and Formation Model
Result of image sampling and quantization

## Slide 13
F(u,v)
Representing Digital images
A beginners guide to bitmaps: http://paulbourke.net/dataformats/bitmaps/

## Slide 14
Representing Digital images

## Slide 15
Original image
Greyscaled image
With OpenCV:
Mat img = imread(filename, 0);
Representing Digital images

## Slide 16
The intensity function

## Slide 17
Representing Digital images

## Slide 18
Plotted as surface
Visual intensity array
(0..0,5..1) =(black, gray and white)
Representing Digital images

## Slide 19
Dark pixels
Light pixels
Histograms

## Slide 20
Pixel by pixel processing
Image Processing
Taking an input image I, pumping every pixel in a function f,
and put the result to an output image O.

## Slide 21
Thresholding
If pixelvalue < t
then pixelvalue := 0;
If pixelvalue >= t
then pixelvalue := 1;
t = threshold value
x,y = pixelcoordinate
Calculating the threshold value t… ?

## Slide 22
Dark pixels
Light pixels
Calculating the threshold value t….
t

## Slide 23
Spatial operations
Image Processing

## Slide 24
Example spatial operations
Median filter.
Image Processing
smoothing
W

## Slide 25
Image Processing
smoothing
Example spatial operations
Mean filter.
117

## Slide 26
Image Processing
edge detection
A very important spatial operation
calling convolution*
-1
0
1
-2
0
2
-1
0
1
1
2
1
0
0
0
-1
-2
-1
Horizontal changes
Vertical changes
= convolution

## Slide 27
Image Processing
?

## Slide 28
Image Processing
a blob is a region of a digital image in which some properties are constant or vary within a prescribed range of values; all the points in a blob can be considered in some sense to be similar to each other.

## Slide 29
Image Processing
More Blobs

## Slide 31
0 0 order;
which is the number of pixels (or Area)
Moments
See also document Simple ImageAnalysis by Moments on SharePoint
an image moment is a certain particular weighted average (moment) of the image pixels, intensities, or a function of such moments, usually chosen to have some attractive property or interpretation.
OpenCV:
http://docs.opencv.org/modules/imgproc/doc/structural_analysis_and_shape_descriptors.html?highlight=moments#moments

## Slide 32
The centroid or centre of mass or gravity is given by
Moments
% im = image
>> m00=mpq(im,0,0)
m00 =
7845
>> m01=mpq(im,0,1)
m01 =
1569000
>> m10=mpq(im,1,0)
m10 =
1569000
>> m01/m00
ans =
200
>> m10/m00
ans =
200
Note: these functions are Matlab functions

## Slide 33
Moments
exercise
A blob has the following moments:
m00 = 6.342.
m01 = 756.492.
m10 = 2331.673.
What is the area of the blob?
  If the blob was circular what is the diameter?
What is the centroid of the blob?
The Area = 6.342 pixels
If the blob was circular then the Area would be giving a diameter of
90 pixels.
Centroids are: (368)
      (119)
Exercise solution:

## Slide 34
Readings (selfstudy)
Chapter 1 up to 4
Learning OpenCV Computer Vision with the OpenCV Library. Gary Bradski & Adrian Kaehler ISBN: 978-0-596-51613-0
See also document: “IntroductionOpenCV.pdf” on SharePoint

## Slide 35
Example1 (Sharepoint)
C++ Interface
Example 2 (Sharepoint)
Drawing shapes and texts
Some examples with OpenCV
Assignment for next week

## Slide 36: OpenCV
OpenCV Wiki
  http://opencv.willowgarage.com/wiki/Welcome
Installation
  OpenCV is integrated in ROS…..(tricky) otherwise
  http://opencv.willowgarage.com/wiki/InstallGuide#GetOpenCV
Tutorials
  A lots available on internet
  http://www.pages.drexel.edu/~nk752/tutorials.html
Assignment for next week: Configure OpenCV in ROS and execute example 1 and example 2 of SharePoint

## Slide 37
End of MINES-VIS 1